Department of Computer Engineering

Faculty of Engineering

Khon Kaen University

### Experiment DSP-05:	Discrete Fourier Transform (DFT)

## Objectives:

- To study and investigate the Discrete Fourier Transform

- To learn how to implement the operation using MATLAB

- To learn how to analyze discrete-time signal using DFT

- To learn how to synthesize discrete-time signal using IDFT

## Introduction:

The discrete-time Fourier transform, DTFT, provided the frequency-domain representation for absolutely summable sequences. The transformation is a function of the continuous variable (() and defined for infinite-length sequences, which is impractical. In other words, the discrete-time Fourier transform is not numerically computable transform.

Therefore we turn our attention to a numerically computable transform. It is obtained by sampling the discrete-time Fourier transform in the frequency domain. When applied to finite-duration sequences, this gives us a new transform, called the Discrete Fourier Transform (or DFT). The DFT is the ultimate numerically computable Fourier transform for arbitrary finite-duration sequences.

The Discrete Fourier Transform of an N-point sequence is given by

where . Note that the DFT is also an N-point sequence, that is, it is not defined outside

The inverse discrete Fourier transform (IDFT) of an N-point DFT is given by (once again is not defined outside)

In MATLAB, an efficient implementation of the both transforms, DFT and IDFT, would be to use a matrix-vector multiplication for each of the relations in (1) and (2).If and are arranged as row vectors x and X, respectively, then from (1) and (2) we have

(3)

(4)

where  and  are a DFT matrix and its conjugate, respectively. The following MATLAB functions implement the above equations.

function [Xk] = dft(xn, N)

% Computes Discrete Fourier Transform

% ----------------------------------------------

% [Xk] = dft(xn, N)

% Xk = DFT coeff. Array over 0 <= k <= N-1

% xn = N-point finite-duration sequence

%  N = Length of DFT

%

n = [0:1:N-1];		% row vector for n

k = [0:1:N-1];		% row vector for k

WN = exp(-j*2*pi/N);	% Wn factor

nk = n’*k;			% creates a NxN matrix of nk values

WNnk = WN .^ nk;		% DFT matrix

Xk = xn * WNnk;		% row vector for DFT coefficients

% End of function

function [xn] = idft(Xk, N)

% Computes Inverse Discrete Fourier Transform

% -------------------------------------------

% [xn] = idft(Xk, N)

% xn = N-point sequence over 0 <= n <= N-1

% Xk = DFT coeff. Array over 0 <= n <= N-1

%  N = Length of DFT

%

n = [0:1:N-1];		% row vector for n

k = [0:1:N-1];		% row vector for k

WN = exp(-j*2*pi/N);	% Wn factor

nk = n’*k;			% creates a NxN matrix of nk values

WNnk = WN .^ (-nk);	% IDFT matrix

xn = (Xk*WNnk)/N;		% row vector of IDFT values

% End of function

Experiment:

- For the sequence , which has DTFT as in the appendix, use the following MATLAB commands to compute its DFT and record the results.
>> x = [1, 1, 1, 1]; N = 4;
>> X = dft(x, N);
>> magX = abs(X), phaX = angle(X)*180/pi

- Plot the magnitude and phase of the DFT in (1) versus k (using the supplot com
mand is recommended). In this case the value k is identical to n. (Note: Save the plot for used in a report.)

- Apply the zero-padding operation, which is a technique that allows us to sample at dense (or finer) frequencies, to get an 8-point sequence and then compute its DFT by using the following MATLAB commands.
>> x = [1, 1, 1, 1, zeros(1,4)]; N = 8;
>> X = dft(x, N);
>> magX = abs(X), phaX = angle(X)*180/pi

- Record the results of (3) and plot the magnitude and phase of the 8-point DFT versus k. (Note: Save the plot for used in a report.)

- Treat thein (1) as a 16-point sequence by padding 12 zeros instead of 4 zeros as in (3).

- Plot the magnitude and phase of the 16-point DFT versus k. (Note: Save the plot for used in a report.)

- For the sequence , use the following MATLAB commands to determine the 10-point DFT of to obtain an estimate of its DTFT. (Note: Save the plot for used in a report.)

>> n = [0:1:99]; x = cos(0.48*pi*n)+cos(0.52*pi*n);
>> n1 = [0:1:9]; y1 = x(1:1:10);
>> subplot(2, 1, 1); stem(n1, y1); 
>> title(‘signal x(n), 0 <= n <= 9’);
>> xlabel(‘n’);
>> Y1 = dft(y1, 10); magY1 = abs(Y1(1:1:6));
>> k1 =  0:1:5; w1 = 2*pi/10*k1;
>> subplot(2, 1,  2); plot(w1/pi, magY1);
>> title(‘Samples of DFT Magnitude’);
>> xlabel(‘frequence in pi units’);

- Use the following commands to pad 90 zeros and obtain a dense spectrum of the . (Note: Save the plot for used in a report.)
>> n2 = [0:1:99]; y2 = [x(1:1:10) zeros(1,90);
>> subplot(2, 1, 1); stem(n2, y2); 
>> title(‘signal x(n), 0 <= n <= 9 + 90 zeros’);
>> xlabel(‘n’);
>> Y2 = dft(y2, 100); magY2 = abs(Y2(1:1:51));
>> k2 =  0:1:50; w2 = 2*pi/100*k2;
>> subplot(2, 1, 2); plot(w2/pi, magY2);
>> title(‘DFT Magnitude’);
>> xlabel(‘frequence in pi units’);

- Use the following commands to take the first 100 samples of and determine its DTFT. (Note: Save the plot for used in a report.)
>> subplot(2, 1, 1); stem(n, x); 
>> title(‘signal x(n), 0 <= n <= 99’);
>> xlabel(‘n’);
>> X = dft(x, 100); magX = abs(X(1:1:51));
>> k =  0:1:50; w = 2*pi/100*k;
>> subplot(2, 1, 2); plot(w/pi, magX);
>> title(‘DFT Magnitude’);
>> xlabel(‘frequence in pi units’);

- Use the following commands to synthesize the sequence using the Inverse Discrete Fourier Transform (IDFT).

>> x1 = idft(X, 100);

>> subplot(2, 1, 2); stem(n, x1);
>> title(‘Synthesized x(n)’);
>> xlabel(‘n’);

Questions:

1. Shows the general form of the matrix  in the Equation (3).

2. How can we get the high-density spectrum?

3. How can we get the high-resolution spectrum?

Appendix

Let be a 4-point sequent:

The discrete-time Fourier transform (DTFT) is given by

Hence

and

________________________________________________________________________

Nawapak Eua-anant and Rujchai Ung-arunyawee

10 January 2549

Name:______________________________________________________________ID:________________

##### In class assignment DSP05

1.  What is the size of Matrix  in Equation (3)?

2. What is the effect of zero padding on  X(k), explain briefly ?

3. Explain the disadvantage point of computing Discrete Fourier Transform directly from equation

4. What knowledge do you get from this lab?